## Slide 1: Terrain Analysis using GIS
Sulochan Dhungel
04/07/2022

## Slide 2: Overview
Watershed delineation (Intro) – 5 min
How does GIS do it? – 10 ~ 15 min
Steps to be followed (as GIS demo) – 10 min
Limitations of this approach – 5 min
Tool created (as demo of the tool) – 10 ~ 15 min
Some other uses of terrain analysis tools – 5~10 min

## Slide 4: How to delineate a watershed
Step 1: Draw a circle at downstream outlet
Step 2: Draw small X’s at high points, ridge lines and saddles
1
2
USDA guidelines to delineate a watershed

## Slide 5: How to delineate a watershed
Step 1: Draw a circle at downstream outlet
Step 2: Draw small X’s at high points, ridge lines and saddles
Step 3: Draw a line starting at circle through these points which crosses each contour line at right angles until you get back to the circle
3
USDA guidelines to delineate a watershed
Notes: Many times, this could be adequate.

## Slide 6: Watershed
Any drop of water that falls in the watershed reaches the outlet!
3
USDA guidelines to delineate a watershed
Notes: Many times, this could be adequate.

## Slide 7
Better data and visualization has made it easier
ESRI Topo with hillshade
USGS Topo with contours and hillshade

## Slide 8
Better data and visualization has made it easier
ESRI Topo with hillshade
USGS Topo with contours and hillshade

## Slide 9: Where is GIS useful?
When there are a lot of watersheds to be delineated
Figure from Highline Canal Stormwater Masterplan project
Notes: This is a figure which shows watersheds delineated for Highline canal stormwater masterplan project.

## Slide 10: Where is GIS useful?
When there are a lot of watersheds to be delineated
In urban areas where topographical high points are difficult to ascertain and takes a long time
Figure from Highline Canal Stormwater Masterplan project
Notes: This is a figure which shows watersheds delineated for Highline canal stormwater masterplan project.

## Slide 11: Where is GIS useful?
When there are a lot of watersheds to be delineated
In urban areas where topographical high points are difficult to ascertain and takes a long time
GIS approach enables derivation of variety of information useful for hydrological and geomorphological processes and model inputs
Notes: Water retention after rainfall, Drainage densities of sub-watersheds, stability index mapping of landslides and much more

## Slide 12: Terrain data (Contours)
Contours: Build using Triangular Irregular Network (TIN)
Notes: We’ve seen contours and we have see that they’re built using TINs

## Slide 13: Terrain data (Contours)
Contours: Build using Triangular Irregular Network (TIN)
Survey or LIDAR
Points
Triangles
Surface
Contours
Notes: We saw how watershed was delineated using contours.
We’ve seen contours – and usually in CAD, we see that they’re built using survey data and TINs

## Slide 14
Contours: Build using Triangular Irregular Network (TIN)
Survey or LIDAR
Points
Triangles
Surface
GRID/ Raster
Terrain data (GRID/Raster)
Notes: We saw how watershed was delineated using contours.
We’ve seen contours – and usually in CAD, we see that they’re built using survey data and TINs

## Slide 15: Terrain Data (GRID/Raster)
A grid is created over TIN surface

## Slide 16: Terrain Data (Raster)
Elevation values from TIN surface within center of each grid are interpolated

## Slide 17: Terrain Data (Raster)
Elevation values from TIN surface within center of each grid are interpolated

## Slide 18: Terrain Data (Raster)
Visualization of raster is done based on the values

## Slide 19: Terrain Data (Raster)
Visualization of raster is done based on the values
USGS, NOAA and other agencies produce and distribute these raster datasets. It can be downloaded and used directly in GIS.

## Slide 20: Terrain analysis using GIS
Terrain raster is just a table of elevation values

## Slide 21: Terrain analysis using GIS
Terrain raster is just a table of elevation values
(Let’s take a subset)
80
74
63
69
67
56
60
52
48

## Slide 22: Terrain analysis using GIS
Terrain raster is just a table of elevation values
We want to figure out how a drop of water travels across the grid
80
74
63
69
67
56
60
52
48

## Slide 23: Terrain analysis using GIS
Terrain raster is just a table of elevation values
We want to figure out how a drop of water travels across the grid
80
74
63
69
67
56
60
52
48
30
Slope

## Slide 24: Terrain analysis using GIS
Terrain raster is just a table of elevation values
We want to figure out how a drop of water travels across the grid
80
74
63
69
67
56
60
52
48
30
Steepest Slope

## Slide 25: Terrain analysis using GIS
Terrain raster is just a table of elevation values
We want to figure out how a drop of water travels across the grid
The flow directions for all grid cells are determined.
Flow Direction Grid

## Slide 26: Terrain analysis using GIS
Using the flow direction grid, a flow accumulation grid is created
0
0
2
2 cells draining

## Slide 27: Terrain analysis using GIS
Using the flow direction grid, a flow accumulation grid is created
0
0
2
0
0
2
0
0
2
2 cells draining
2 cells draining

## Slide 28: Terrain analysis using GIS
Using the flow direction grid, a flow accumulation grid is created
0
0
2
0
0
2
0
0
2
0
0
2
0
0
0
0
2
2
2 cells draining
2 cells draining
2 cells draining

## Slide 29: Terrain analysis using GIS
Using the flow direction grid, a flow accumulation grid is created
0
0
2
0
0
0
0
2
2
0
10
6 cells accumulated
+
4 cells draining

## Slide 30: Terrain analysis using GIS
The flow accumulation grid is created
4
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
1
19
1
0
0
2
0
0
0
0
2
2
0
10
Flow accumulation grid
6 cells accumulated
+
4 cells draining

## Slide 31: Terrain analysis using GIS
The flow accumulation grid creates a network grid
4
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
1
19
1
0
0
2
0
0
0
0
2
2
0
10
Flow accumulation grid
6 cells accumulated
+
4 cells draining
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
Network grid
Notes: This network grid is the basis of delineation of streams and catchments

## Slide 32: Terrain analysis using GIS
Stream delineation – where does the streamline start from?

## Slide 33: Terrain analysis using GIS
Define what a stream is based on flow accumulation
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1

## Slide 34: Terrain analysis using GIS
Define what a stream is based on flow accumulation
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Assume Flow Accumulation > 10 Cell Threshold

## Slide 35: Terrain analysis using GIS
Define what a stream is based on flow accumulation
Stream Network

## Slide 36: Terrain analysis using GIS
Define what a stream is based on flow accumulation
Watershed
Watershed
Outlet

## Slide 37: Terrain analysis using GIS
Define what a stream is based on flow accumulation
This process is repeated on the raster dataset using GIS
Watershed
Outlet

## Slide 38: GIS Demo

## Slide 39: GIS Demo
Elevation

## Slide 40: GIS Demo
Direction Encoding (D8)
32
16
8
64
4
128
1
2
The results are only 8 integer values representing each direction

## Slide 41: GIS Demo
Direction Encoding (D8)
32
16
8
64
128
4
128
1
2
The results are only 8 integer values representing each direction
32
16
8
64
4
128
1
2

## Slide 42: GIS Demo
Direction Encoding (D8)
32
16
8
64
4
128
1
2
The results are only 8 integer values representing each direction
32
16
8
64
4
128
1
2

## Slide 43: GIS Demo
Direction Encoding (D8)
32
16
8
64
128
4
128
2
2
The results are only 8 integer values representing each direction
32
16
8
64
4
128
1
2

## Slide 44: GIS Demo
Direction Encoding (D8)
32
16
8
64
4
128
1
2
The results are only 8 integer values representing each direction
32
16
8
64
4
128
1
2

## Slide 45: GIS Demo
Direction Encoding (DINF)
The results are angle value from east
‘Flow accumulation’ tool takes input from either D8 or DINF currently in ArcGIS
Notes: MFD => Multiple Flow Direction => has potentially multiple values tied to each cell => Each value corresponds to proportion of flow to each downstream neighbor => not easily visualized
Drop Raster => Slope as percentage => ratio of the maximum change in elevation from each cell along the direction of flow to the path length between centers of cells, expressed in percentages.
Force all edge cells to flow outward => Since we can’t confirm the flow direction of edge cells, we can force all edge cells to outward
We will only work with D8 for most of hydrological analysis, although most of the subsequent analysis can be done using DINF also.

## Slide 46: Back to GIS Demo

## Slide 47: GIS Demo
Problem with Flow direction at certain cells
To remove those sinks we “Pit fill”

## Slide 48: Pit Filling of Terrain
Local sinks are usually a problem when DEMs are created.
These sinks need to be filled before creating stream network since they can cause isolated watersheds.

## Slide 49: Pit Filling of Terrain
Original DEM
There are pits where elevations is lower than surrounding cells
When flow direction and accumulation are calculated in these locations, the network delineation cannot propagate out of sink.
Pits OR Sinks

## Slide 50: Pit Filling of Terrain
Pit Filling -> Increase elevation to the pour point elevation until the pit drains to a neighbor
Pit filling needs to be done before starting terrain analysis
Pour Points
The lowest grid cell adjacent to a pit

## Slide 51: Back to GIS demo
Pit Filling
Flow Direction
Flow accumulation
Watershed
Stream-line delineation
  5.1 CON (gt 50K)
  5.2 Stream LINK
  5.3 Watershed

## Slide 52
Hydrologic processes are different on hillslopes and in channels. It is important to recognize this and account for this in the delineation of streams.
Drainage area can be concentrated or dispersed (specific catchment area) representing concentrated or dispersed flow.
So, threshold method is not always the best.
There are other ways to delineate network (1) Support area method or (2) Pueker Douglas

## Slide 53: Back to GIS demo
Pit Filling
Flow Direction
Flow accumulation
Watershed
Stream-line delineation
  5.1 CON (gt 50K)
  5.2 Stream LINK
  5.3 Watershed
  5.4 Stream Order (Use link raster to preserve direction)

## Slide 54: Stream Order
Method of assigning numeric order to stream links
Can be helpful in understanding some characteristics of stream
Example - First order streams are dominated by overland flows – most susceptible to non-point source pollution

## Slide 55: Back to GIS demo
Pit Filling
Flow Direction
Flow accumulation
Watershed
Stream-line delineation
  5.1 CON (gt 100K)
  5.2 Stream LINK
  5.3 Watershed
  5.4 Stream Order (Use link raster to preserve direction)
  5.5 Raster to Polyline
6. Delineate more sub-watersheds if needed

## Slide 56: Fill Issue

## Slide 57: Carving the DEM
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point
This has not been implemented in ArcGIS yet.

## Slide 58: Carving
Pits
Original DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 59: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 60
Filling
Carving
Minimizing Alterations

## Slide 61: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 62: Carving the DEM
This has not been implemented in GIS

## Slide 63: GIS DEMO
Snap Pour Point (Grabs the point with highest flow accumulation within specified radius)
100 feet
Network creation
  Feature dataset
  Create Trace network – edge flow lines
  Enable Network topology
  Validate Network Topology

## Slide 64: Thank you!